## Slide 1
High Correlation, low error.
DRAM reads for these apps have high correlation with low error.
Improving DRAM modeling can decrease the error further.
Low Correlation, high error
Over estimation and high error due to inaccurate caching model.
Cache system modeling needs to be improved.
A Quantitative Evaluation of Contemporary GPU Simulation Methodology
Akshay Jain, Mahmoud Khairy, Timothy G. Rogers
Purdue University, Department of Electrical and Computer Engineering
akshayj@alumni.purdue.edu, abdallm@purdue.edu, timrogers@purdue.edu
SIGMETRICS 2018
Introduction
We quantify error in the popular GPU architecture simulator, GPGPU-Sim (1100+ citations).
We demonstrate that the simulator's accuracy is highly dependent on the workload type.
Experimental Results
Accelerator Architecture Lab at Purdue
Simulator supports 2 ISA representations of each app: a modern virtual ISA (vISA) and the machine ISA (mISA) for the decade old GT200 architecture.
vISA has infinite registers, is generally less optimized and more abstract.
vISA is called PTX and the GT200 mISA is PTXPlus
Workload Characteristics
Case Study
Performance predictions for an architectural study can vary depending on the ISA used.
mISA models the memory traffic due to register spilling (as it is register allocated).
We see performance improvement for HOT and BS only with the mISA.
Cache Sensitive
Memory Sensitive
Compute Intensive
Compute Balanced
Chart: Norm. Dynamic Instr. Count wrt HW
| vISA | mISA | vISA | mISA | vISA | mISA | vISA | mISA | vISA | mISA | HWL | STN | SMM | CP | MRI | Compute-Intensive
ALU_OP | 0.27252 | 1.0292 | 0.55768 | 0.68366 | 1.4538 | 0.17808 | 0.77747 | 0.69226 | 0.53115 | 0.32329
MAD_OP | 0.025158 | 0.17542 | 0 | 0.14316 | 0.5981 | 0.60068 | 0.14905 | 0.23955 | 0.28264 | 0.28674
Control_OP | 0.016578 | 0.066045 | 0.07839 | 0.11471 | 0.04668 | 0.046854 | 0.094006 | 0.044673 | 0.03547 | 0.035976
SFU_OP | 0 | 0.024505 | 0 | 0 | 0 | 0 | 0.04305 | 0.052906 | 0.14132 | 0.14333
MEM_OP | 0.063113 | 0.049608 | 0.20798 | 0.046675 | 0.64576 | 0.043378 | 0.27545 | 0.0023162 | 0.31895 | 0.00049647
Tex_OP | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
NOP_OP | 0 | 0.0011954 | 0 | 0.043026 | 0 | 0 | 0 | 0.0093964 | 0 | 0.071667
Execution cycles in simulation relative to hardware. Figure shows a breakdown of stalls and useful execution from GPGPU-Sim.
High correlation and low error with mISA.
mISA (even if old) is better than vISA.
mISA has high correlation wrt dynamic inst breakdown.
Supporting new mISA can improve correlation further.
Better results with vISA in certain apps.
vISA is able to hide the deficiencies of the old mISA.
Z5 kernel in SRAD1 uses one instruction in vISA for integer division, which gets expanded into 33 instructions in the old mISA
Type | IPC | L1 Miss | L2 Miss | Mem Util
cache-sensitive | Low | High | Mod | Low
memory-sensitive | Mod | High | High | High
compute-intensive | High | Mod | Mod | Mod
compute-balanced | Mod | Mod | Mod | Mod
Chart: Hardware
Chart: Normalized Speedup
| BFS | GMV | HOT | BS
GTO | 1 | 1 | 1 | 1
CCWS | 1.5212 | 2.7342 | 1 | 1
Chart: Normalized Speedup
| BFS | GMV | HOT | BS
GTO | 1 | 1 | 1 | 1
CCWS | 1.3647 | 2.1125 | 1.0651 | 1.2541
(a) Speedup using vISA (b) Speedup using mISA